## Slide 1: 3D-GIS & Small Body Mapping Tool
N. Hirata (Univ. of Aizu)
Notes: <number>

## Slide 2: Mapping asteroids
How to represent map information of small bodies
Spherical Bodies
  Map projection from spherical body to plane
    major GISs
Notes: Let’s move on another topic in my talk.
We also grapple with a task how to represent map information of irregular shaped small bodies.
A problem same on location-oriented search rises on this task.
For spherical bodies, we usually use a plane paper map or its mimic on PC display. Geographical information are projected by a specific projection method onto a plane. Such projection methods are developed for spherical or ellipsoidal bodies, so they are based on a spherical coordinate. It cannot apply to an irregular-shaped body.
<number>

## Slide 3: 平面の地図表現

## Slide 4
Itokawa
Notes: The asteroid Itokawa, the target of the Hayabusa mission, has an extremely non-spherical shape. On Itokawa, the traditional geographic coordinate system do not work well.
<number>

## Slide 5
Itokawa
Multiple intersections at the surface
Non-unique representation of locations!
COM: the origin
of the coordinate
Notes: The origin of the coordinate is the center of mass of the asteroid. Latitude and longitude are defined by the direction of the vector to the certain point on the surface. However, the vector may have multiple intersections at the surface. In this case, the uniqueness of the Latitude and longitude representation is broken. So we need an alternative way to describe locations on the surface of irregular-shaped bodies.
<number>

## Slide 6: Mapping asteroids
Spherical Bodies
  Perspective view of a virtual globe
    Google Earth, NASA WorldWind
Notes: Recently, tools so called virtual globe are developed. Google Earth or NASA WorldWind are major examples of this category of tools. virtual globes provide perspective view of the target body, and also are able to display various mapping data as texture data on the globe.
<number>

## Slide 7: Mapping asteroids
SMBT
Irregular shaped small bodies
  Perspective view of a virtual asteroid
  3D-GIS
  Small Body Mapping Tool (SMBT) by APL/JHU
Notes: This perspective view concept can be applied to irregular shaped bodies. We named such tools as 3D-GIS, and developed a web application with this concept. It also should be noted that APL NEAR-shoemaker group has developed similar tool, Small body mapping tool (SMBT) with this concept.
<number>

## Slide 8: 3D-GIS
Java applet with JOGL
  Java Binding for the OpenGL API
Shape model
  By Bob Gaskell
  49152 polygons
Layers
  Gravity potential
  Slope
  Visible brightness
  NIR reflectance
  Space weathering index
http://sirius.u-aizu.ac.jp/k-sys/3DGIS2_Javaapplet/3DGIS2.html
セットアップ情報:
http://sirius.u-aizu.ac.jp/k-sys/3DGIS2_Javaapplet/JOGL.html
Notes: This is a snap shot of our 3D-GIS web application. This tool is developed with Java and OpenGL. You can see a shape model of Itokawa developed by Bob Gaskell displayed here. The model has about 50 thousand polygons. Layers of map data available now are gravitational potential, slope, visible brightness, NIR reflectance, and space weathering index derived from visible and NIR data. In this snapshot, local slope that defined by gravitation vector and polygon normal is displayed.
<number>

## Slide 9: Functions
Manipulate 3D model
  rotate
  zoom
Mapping layers
  control color LUT
Lat/Lon grid
Local information of all layers
http://sirius.u-aizu.ac.jp/k-sys/3DGIS2_Javaapplet/3DGIS2.html
Notes: User can manipulate this 3D model by mouse operation. It can rotate, it can zoom-in and zoom-out. User also control look-up-table of mapping layers by these sliders. Even though there are local failure on uniqueness of latitude/longitude values, the lat/lon grid is helpful for guidance for users. Physical values of every layers at a specific location are displayed here.
<number>

## Slide 10: Small Body Mapping Tool: SMBT
Johns Hopkins Univ.のApplied Physics Lab (JHU/APL)で開発
コンセプトとしては会津大の3D-GISとほぼ同一
負けている機能もあるw
  画像の形状モデルへのマッピング
  形状モデル上へのマーキング（研究者向け版のみ）

## Slide 11: SMBT
一般向け
http://near.jhuapl.edu/software/sbmt/

## Slide 12: 3D-GISで独自マッピングデータを表示する
Eclipse上でApplet版のソースコードを動作させることができる
データの入れ替え，ソースコードの改変が可能